## Slide 1
AgrIoT
By:
K.Kirishikesan
01/05/2020

## Slide 2: Introduction
A network of sensor nodes which collect data such as humidity, temperature, moisture gradient, light intensity and electrical conductivity and an airborne drone which collects image data and integrates the system for data analysis.
Parts of the project:
  Sensor nodes
  Mesh network of nodes
  Communication protocol between node and drone
  Drone
  Data analysis
01/05/2020

## Slide 3: Phase 1
  Done by:
    Aruna Jayasena
    Radershan Suguneswaran
    Ketharan Suntharam
    Thiru Ashok
  Created a prototype for Sensor Node with a custom sensor for Electrical conductivity
  Created an app with cloud storage for data collection from a single node
  Created drone based image data collection
01/05/2020

## Slide 4: Phase 2
  Done by:
    A.L.D.S. Liyanage
    K.Kirishikesan
  A communication protocol between sensor nodes and the drone
  Mesh network of nodes
01/05/2020

## Slide 5: Power Consumption of protocol in phase 2
HC12- sleep………………….80µA
HC12- transmission……..3.6mA
Stm32f103c8t6…………….8mA
Total current consumption per hour:29.6928A
6 months:5344.704
Needed battery:494mAh battery
01/05/2020

## Slide 6: Phase 3
  By:
    K.Kirishikesan
  Production ready sensor nodes
  Dynamic mesh network functionality
  Communication protocol to communicate with the drone
01/05/2020

## Slide 7: Work breakdown
Mesh network creation
Communication protocol
Implementation of protocol
Implementation of Sensor node
Enclosure design
Enclosure printing
Electrical conductivity sensor design
RFC
PCB design
PCB printing
Assembly and finish
01/05/2020

## Slide 8: Sensor node
Sensor node is equipped with the following sensors
DHT22/AM2302 Temperature & Humidity sensor
BH1750 Light Intensity sensor
YL69 Soil moisture sensor
01/05/2020

## Slide 9: Enclosure
01/05/2020

## Slide 10: Mesh network creation
01/05/2020

## Slide 11: Send data as to master
01/05/2020

## Slide 12: Receive data as master from other nodes
01/05/2020

## Slide 13: Implementation issues and solutions
  Multiple masters: Every master will keep a list of all the node ids that were synced with this master and will discard any message send from any other nodes and will not respond
  Master role switch: As the master will be continuously keeping its radio on, the master role will be switched after every 4 hours. The slaves which are connected to the master will try to send data in their next round but will fail to receive acks and then declare themselves master. After an hour they will start synchronization again and eventually be part of the network
  Hidden node problem: The node will declare itself a master
  Too much traffic: Only the masters will transfer data to the drone
  Power fluctuation if radio is on for more than 5 days: every 4 hours master role will be switched.
01/05/2020

## Slide 14: Frame Structure when in sync state
1 bit to identify state
8 bit sender id
8 bit receiver id
Content:Timestamp
4bit Error bits(even parity in blocks)
01/05/2020

## Slide 15: Frame Structure when in Data-transfer state
1 bit to identify state
3 bit code to identify type of frame
8 bit drone id
8 bit node id
Content: Data or initial or final sequence number of transmission
4bit Error bits(even parity in blocks)
01/05/2020

## Slide 16: Frames and their identification codes
Wake-up frame(001)
Request frame(010)
Response frame(011)
Data frame(100)
Ack frame(101)
Retransmission frame(110)
Termination frame(111)
Switchrole frame(000)
01/05/2020

## Slide 17: Message based Synchronization
Time of slave node will be reset to = t4+ ((t2-t1)+(t4-t3))/2
Other
node
Master
node
01/05/2020

## Slide 18: Communication protocol
01/05/2020

## Slide 19: Progress
Mesh network creation …………………………. Complete
Communication protocol ………………………. Complete
Implementation of protocol…………………… Pending
Implementation of Sensor node…………….. Pending
Enclosure design……………………………………….Complete
Enclosure printing…………………………………….Pending
Electrical conductivity sensor design …….. Pending
RFC…………………………………………………………….Pending
PCB design……………………………………………....Pending
PCB printing………………………………………………Pending
Assembly and finish………………………………….Pending
01/05/2020

## Slide 20: Next week progress
PCB design
Electrical conductivity sensor integration
01/05/2020

## Slide 21: Week 9 continued…
Redesigned objectives:
  Design Mesh network………………………………………………………………………Complete
  Design Communication protocol between node and drone…………..Complete
  Simulate Mesh network…………………………………………………………………..On Progress
  Simulate Communication protocol………………………………………………….On Progress
  Combine Simulations……………………………………………………………………….Incomplete
  Include power consumption calculation with the simulation…………Incomplete
  Prepare an RFC…………………………………………………………………………………Incomplete
08/05/2020

## Slide 22: Redefined Deliverables
  Working Simulations of mesh network and communication protocol
  Complete RFC
08/05/2020

## Slide 23: This week’s progress
  Familiarized myself with Omnet++ Discrete Event Simulator Framework
  Unique id solution for the mesh network design.(Using mac-id)
  Completed two simple simulations.
    Drone to master node communication (One drone and one master)
    Drone to master communication (One drone and 4 masters)
08/05/2020

## Slide 24: Lifecycle of the node
08/05/2020

## Slide 25: Simulations
08/05/2020

## Slide 26: Next week goals
  Complete the simulation taking into account,
    Jitter
    Propagation delay
    Signal strength and distance
    Time to switch on radio
  Build a submodule to calculate power consumption
08/05/2020

## Slide 27: Week 10
Objectives:
  Design Mesh network………………………………………………………………………Complete
  Design Communication protocol between node and drone…………..Complete
  Simulate Mesh network…………………………………………………………………..On Progress
  Simulate Communication protocol………………………………………………….On Progress
  Combine Simulations……………………………………………………………………….Incomplete
  Include power consumption calculation with the simulation…………Incomplete
  Prepare an RFC…………………………………………………………………………………Incomplete
15/05/2020

## Slide 28: This week’s progress
  Explored INET framework
  Analyzed 3 simulations
    Client Server based TCP communication between n nodes
    Ethernet bus communication communication between n nodes
    WLAN communication 2.4GHz and 5GHz.
  Proposed a design structure for the sensor node and the drone
15/05/2020

## Slide 29: Why INET?
  Message passing communication between modules
  Layered communication(OSI model)
  Radio Medium can be modelled
  Has inbuilt components for integration
15/05/2020

## Slide 30: Simulations
15/05/2020

## Slide 31: Design structure of a Wired Computer
15/05/2020

## Slide 32: Design structure of a Wireless Computer
15/05/2020

## Slide 33: Proposed Structure of the Node
15/05/2020

## Slide 34: Next Week Goals
  Build Two Nodes with the proposed Structure (Without Enhanced Shockburst)
  Pass Structured Messages
15/05/2020

## Slide 35
Thank you!