## Slide 1
Plants-speak
By:
A.L.D.S.Liyanage
K.Kirishikesan

## Slide 2: Introduction
A reliable, low power, low cost communication protocol designed for the communication between a cluster of nodes and a moving host.
Low power: #The nodes are in the sleeping mode until an interrupt broadcast is sent to wake it up and transfer the data.
Reliable: #Retransmission frame #Parity bit
Low cost: #An application layer protocol that can handle general datalink layer protocol, which we are free to choose from.
Moving host: #Small data frames #Cyclic memory buffer #If transmission not terminated, node stops the transmission

## Slide 3: Frames
Wake-up frame(001)
Request frame(010)
Response frame(011)
Data frame(100)
Ack frame(101)
Retransmission frame(110)
Termination frame(111)
Configuration frame(000)

## Slide 4: Frame Structure
3 bit code to identify type of frame
8 bit Server id
8 bit Client id
Content: Data or initial or final sequence number of transmission
4bit Error bits(even parity in blocks)

## Slide 5: Collision Handling
Collision avoidance using time chunks
Unique id*10ms for every client to have offsets to identify time to transmit(Clock drifts will be handled by this)

## Slide 6: Demo

## Slide 7: Power Consumption of implementation
HC12- sleep………………….80µA
HC12- transmission……..3.6mA
Stm32f103c8t6…………….8mA
Total current consumption per hour:29.6928A
6 months:5344.704
Needed battery:494mAh battery

## Slide 8: Possible Enhancements
Auto node cluster management
Coordinator using MQTT

## Slide 9: Node Cluster Management
Auto configuring network #Using Configuration frame- When node is switched on, it transmits its id and the number of members that it is connected with. If a larger number network is found the id is added to the larger number of network

## Slide 10: Coordinator network
MQTT coordinator acting as the client of the network
Nodes collecting and publishing the data to the coordinator and going to sleep.

## Slide 11
Thank you!